QUICKSTART PROCEDURE

Plug RPS into 12 volt power source (ships battery, extra battery, etc)
Verify that the beeper and horn chirp

Set Sequence Select for desired starting sequence.

For rolling start, set Shape Alert Select for desired time.

Depress Sequence Start

IMPORTANT

The horn needs a good electrical connection. While it doesn’t use a lot of power, it does draw 13 amperes for short periods. If the cigarette lighter plug on board is connected to the battery via a small gauge or long length of wire then consider connecting directly to the battery.

TIPS AND TECHNIQUES

Dinghy Starts

To use your watch as a back-up timer, start the sequence at 10 seconds to the minute.

To use your stopwatch as a back-up timer, use the 5-4-3-2-1 countdown to the three minute gun to set the stopwatch.

Rolling Starts

For a rolling start which needs a shape taken down one minute prior to sequence start, try this procedure: At five minutes fifteen seconds prior to sequence start, muffle the horn with your hand and start the sequence. You will get a shape alert at one minute prior to the actual sequence start and the rest of the sequence will proceed normally

# Text boxes

MANUAL

HORN

SHAPE ALERT

SELECT

SEQUENCE

SELECT

SEQUENCE

START

REGATTA PRO-START

RESET

PHC

SYSTEMS

www.phcsystems.com

Depress and release to determine the sequence you are in.

Depress and hold to cycle through the sequences.  Release when you are at the desired sequence.

Depress and release to determine the seconds  for shape alert.

Depress and hold to cycle through the shape alert values

Release when you are at the desired value.

Depress and release to start the selected sequence.

Depress at any time to sound the horn.

Sequences in progress are not affected.

Depress ‘Sequence Select’ and ‘Shape Alert Select’ together to reset any sequence in progress.

30 second shape alert

40 second shape alert

50 second shape alert

60 second shape alert

BEEPER RESPONSE

RRS  2 minute Dinghy start

RRS  3 minute Dinghy start

ICYRA 2 minute Dinghy start

ICYRA 3 minute Dinghy start

2 minute rolling start

3 minute rolling start

5 minute rolling start

PRO-START will continue to cycle through the rolling start sequence until the ‘Reset’ buttons are pressed to stop sequence or the unit is unplugged.

2 minute

3 minute

4 minute

Alerts as necessary

Sequence Start

START CLASS

Hoist Shape

GUN

15 Seconds Seconds

5-4-3-2-1

Drop Shape Alert

15 Seconds Seconds

5-4-3-2-1

Beeper alerts for RC

Shape Alert

Sequence

30 to 60 second selectable Shape Alert to prepare to drop shape

Continuous loop back to GUN

GUNS AND BEEPER ALERTS

2, 3, AND 5 MINUTE ROLLING START SEQUENCE

15 Seconds Seconds

5-4-3-2-1

1 minute 30 Seconds

2 minutes

3 minutes

30 Seconds

1 minute

START

5-4-3-2-1

20 Seconds

10 Seconds

3 Minutes 10 Seconds

GUNS

2 and 3 MINUTE DINGHY START

5-4-3-2-1 beeper countdown for these guns

Sequence does one cycle and ends.  Hit ‘Sequence Start’ button to re-start sequence.

2 minute sequence

eliminates the first

minute.

RRS sequence has 1 short

ICYRA sequence has 3 short

Sequence Start

NOTE:

The beeper chirps at ten second intervals during all sequences