| QUICKSTART PROCEDURE Turn the “ON/OFF” switch on the battery pack to “ON”, Verify that the beeper and horn chirp Set Sequence Select for desired starting sequence. Set Shape Alert Select for desired ‘Alert’ time. Depress Sequence Start IMPORTANT Keep the battery charged. A battery left partially discharged will lose energy over time due to sulphation. . | Shape Alert Button This button has different meanings for each sequence as follows: 1, 2, & 3 min Dinghy Attention signal tens of seconds prior to first gun 5 Minute Attention signal tens of seconds prior to first gun Match Race Warning signal minutes prior to Prepretaratory gun 2, 3,& 5 min Rolling Shape alert tens of seconds prior to start gun |
| --- | --- |

# Text boxes

MANUAL

HORN

SHAPE ALERT

SELECT

SEQUENCE

SELECT

SEQUENCE

START

REGATTA PRO-START

RESET

PHC

SYSTEMS

www.phcsystems.com

Depress and release to determine the sequence you are in.

Depress and hold to cycle through the sequences.  Release when you are at the desired sequence.

Depress and release to determine the seconds  for shape alert.

Depress and hold to cycle through the shape alert values

Release when you are at the desired value.

Depress and release to start the selected sequence.

Depress at any time to sound the horn.

Sequences in progress are not affected.

Depress ‘Sequence Select’ and ‘Shape Alert Select’ together to reset any sequence in progress.

No shape alert

10 second shape alert

20 second shape alert

30 second shape alert

40 second shape alert

50 second shape alert

60 second shape alert

BEEPER RESPONSE

1 minute Dinghy sequence
2 minute Dinghy sequence

3 minute Apx Q Dinghy sequence

5 minute Rule 26 sequence
Match Race AC sequence

2 minute rolling sequence

3 minute rolling sequence

5 minute (pre 2001) rolling sequence

●●